## Slide 1: UCSD Embedded C Assignment 6
By
Hsuankai Chang
hsuankac@umich.edu

## Slide 2: Step 1. Startup STM32CubeIDE and create new STM32 project

## Slide 3: Step 2. Access board selector and type in the board you use, click Next

## Slide 4: Step 3. Enter the project name then click Next

## Slide 5: Step 4. See the firmware package name and version

## Slide 6: Step 5. Click yes to initialize all peripherals to default

## Slide 7: Step 6. When in .ioc file, click Pinout & Configurations

## Slide 8: Step 7. Observe PC5 -> ADC1_IN14 -> ADR_A0

## Slide 9: Step 8. Set ADC1, IN14 to Single-ended

## Slide 10: Step 9. Generate code

## Slide 11: Step 10. In main.c, find code that initializes the ADC1

## Slide 12: Step 11. In main.c, find code that initialize the channel IN14

## Slide 13: Step 12. Add code to main.c to read from ARD_A0

## Slide 14: Step 13. Build project and run in debug mode

## Slide 15: Step 14, Set the break point, then read the adcResult when nothing connected to ARD_A0. In my case adcResult = 916

## Slide 16: Step 15. Connect ADR_A0 to GND, then adcResult = 0

## Slide 17: Step 16. Connect ADR_A0 to 1.5VDC. Then adcResult = 1856