## Slide 1: UCSD Embedded C Final Assignment
By
Hsuankai Chang
hsuankac@umich.edu

## Slide 2: Step 1. Startup STM32CubeIDE and create new STM32 project

## Slide 3: Step 2. Access board selector and type in the board you use, enter project name and click Next

## Slide 4: Step 3. Click yes to initialize all peripherals to default

## Slide 5: Step 4. When in .ioc file, view the overall default settings

## Slide 6: Step 5. Click GPIO and set PB2 pin as custom_led output push pull pin, we will use this pin to toggle external LED for demo 4

## Slide 7: Step 6. Confirm that blue button has set up as external interrupt trigger

## Slide 8: Step 7. Generate the code, and in main.h file, and the required low layer header file for use in demo 1

## Slide 9: Step 8. Create BSP folder under Drivers folder, and copy and paste the local Components and B-L475E-IOT01 folder to it. This is for using BSP package for temp sensor in demo 3

## Slide 10: Step 9. Add the BSP folder to the include path

## Slide 11: Step 10. In main.c file, add the required header files

## Slide 12: Step 11. In main.c, add the needed variables

## Slide 13: Step 12. Add the function definition for EXTI call back function

## Slide 14: Step 13. Add the code for demo 1 to demo 4

## Slide 15: Step 14. Setup the wire connection for demo 4 LED blinking

## Slide 16: Step 15. Compile and run the code in debug mode, open tera term and test from demo 1. test is successful, print the flash size and device ID once when entering demo 1 code, and continue blinking LED2 at 1 second interval

## Slide 17: Step 16. Press the user button, we will see HAL device ID and unique ID only print once, and continue blinking LED for 2 seconds interval. Demo 2 success

## Slide 18: Step 17. Press the user button again, now we can read the temp value and send it through UART1. Demo 3 success

## Slide 19: Step 18. Press the user button again, we can see the external LED blinking at 4 seconds interval. Demo 4 success

## Slide 20: Step 19. Press the user button again, it will loop back to demo 1