## Slide 1: UCSD Embedded RTOS Assignment 2
By
Hsuankai Chang
hsuankac@umich.edu

## Slide 2: Step 1. Startup STM32CubeIDE and create new STM32 project

## Slide 3: Step 2. Access board selector and type in the board you use, click Next

## Slide 4: Step 3. Enter the project name then click Next

## Slide 5: Step 4. See the firmware package name and version

## Slide 6: Step 5. Click yes to initialize all peripherals to default

## Slide 7: Step 6. When in .ioc file, click Pinout & Configurations

## Slide 8: Step 7. Enable the FreeRTOS in middleware. Configure FreeRTOS for a HEAP memory size of 6000. Keep the default dynamic/static allocation along with the default memory 4 allocation option. Enable the malloc failed hook macro.

## Slide 9: Step 8. Change Timebase from systick to TIM1

## Slide 10: Step 9. In your default task, blink the LED2 every second and also use pvPortMalloc() to allocate 500 bytes every time you blink the LED2.

## Slide 11: Step 10. Add the vApplicationMallocFailedHook() to your code so that when you run out of memory (remember you have a memory leak from in the default task as described in the previous bullet). The code in the vApplication MallocFailedHook() should be a "while (1) { }" that blinks the Wifi/BlE LEDs at a 0.5 second (1/2 second) rate.

## Slide 12: Step 11. Build and run the code, since after several loops, memory leaks occur, so the process will stuck in vApplicationMallocFailedHook and keep blinking WIFI/BLE LED rather than blinking LED2.