## Slide 1: UCSD Embedded RTOS Assignment 3
By
Hsuankai Chang
hsuankac@umich.edu

## Slide 2: Step 1. Startup STM32CubeIDE and create new STM32 project

## Slide 3: Step 2. Access board selector and type in the board you use, click Next

## Slide 4: Step 3. Enter the project name then click Next

## Slide 5: Step 4. See the firmware package name and version

## Slide 6: Step 5. Click yes to initialize all peripherals to default

## Slide 7: Step 6. When in .ioc file, click Pinout & Configurations

## Slide 8: Step 7. Enable the CMSIS_V1 RTOS, and add two more tasks. Set different priority to test

## Slide 9: Step 8. Change Timebase from systick to TIM1

## Slide 10: Step 9. In your default task, blink the LED2 every 250 ms

## Slide 11: Step 10. In task 2, blinks LED3_WIFI_LED4_BLE every 1000 msec

## Slide 12: Step 11. Create "Task 3" that displays a counter (e.g. "count = 1", "count = 2", etc.) on the STM32 Virtual Console.

## Slide 13: Step 12. Debug and run the code, you can see LED2 and LED3 blinking, and console prints out the desired message