## Slide 1: UCSD Embedded C Assignment 8
By
Hsuankai Chang
hsuankac@umich.edu

## Slide 2: Step 1. Startup STM32CubeIDE and create new STM32 project

## Slide 3: Step 2. Access board selector and type in the board you use, click Next

## Slide 4: Step 3. Enter the project name then click Next

## Slide 5: Step 4. See the firmware package name, version and location

## Slide 6: Step 5. Click yes to initialize all peripherals to default

## Slide 7: Step 6. Copy the BLE folder into the project, and delete the HeartRate folder

## Slide 8: Step 7. Delete EWARM and MDK-ARM folder

## Slide 9: Step 8. Add the BLE source path and include path

## Slide 10: Step 9. Copy the missing LL and HAL header and source file into the project, which includes stm32l4xx_ll_pwr.h, stm32l4xx_ll_rtc.h, stm32l4xx_ll_cortex.h, stm32l4xx_ll_spi.h, stm32l4xx_ll_dma.h, stm32l4xx_hal_rtc.h, stm32l4xx_hal_rtc_ex.h

## Slide 11: Step 10. Add stm32l4xx_hal_rtc.h in hw.h file

## Slide 12: Step 11. Add BSP folders into the project, and also add the include path and source path

## Slide 13: Step 12. Add BLUENRG_MS into preprocessor symbols, since our aci_gap_init function use 5 parameters

## Slide 14: Step 13. Change the hal_types.h and hal.h include header files to bluenrg_private_hal_types.h and stm32l4xx_hal.h file in hci_ie.c and bluenrg_I2cap_aci.c file

## Slide 15: Step 14. Add hci_tl_io.h include file into hci_Ie.c file

## Slide 16: Step 15. Delete main.c, stm32l4xx_it.c, system_stm32l4xx.c, stm32l4xx_hal_msp.cand also startup file in Core folder

## Slide 17: Step 16. Delete ble_hci_ti_io_template.c file to solve multiple definition of hci_send_rq function

## Slide 18: Step 17. Add stm32l4xx_hal_rcc, rtc and rtc_ex source files in driver folder, and uncomment HAL_RTC_MODULE_ENABLED to use the feature

## Slide 19: Step 18. Add stm32l4xx_ll_rcc.h file in main.c file under BLE folder to resolve LL_RCC errors

## Slide 20: Step 19. Add stm32l4xx_ll_exit.h and .c file into driver inc and src folder, then add the header file into hw_timerserver.c file

## Slide 21: Step 20. Comment out all the HRS_Notification function in hrs.c file

## Slide 22: Step 21. Finally, we can build the project successfully, and when run in debug mode, we can search the Bluetooth module of our stm board

## Slide 23: Appendix, schematic for BLE module, processor side connection

## Slide 24: Appendix, schematic for BLE module